Totally—here’s a clean, numeric example using Sentinel-1’s C-band.
# Setup
- Carrier frequency f0≈5.405 GHzf_0 \approx 5.405\,\text{GHz} ⇒\Rightarrow wavelength
  λ=cf0≈0.05547 m\displaystyle \lambda=\frac{c}{f_0}\approx 0.05547\,\text{m} (5.55 cm).
- For a moving target, the along-track (azimuth) velocity vazv_{az} relates to the Doppler centroid shift Δfd\Delta f_d by
  vaz  ≈  −λ2 Δfd⇔Δfd  ≈  −2λ vaz.v_{az}\;\approx\;-\frac{\lambda}{2}\,\Delta f_d \quad\Leftrightarrow\quad \Delta f_d\;\approx\;-\frac{2}{\lambda}\,v_{az}.
# Example 1 — a ship at 10 m/s along-track
Δfd≈−20.05547×10  ≈  −361 Hz.\Delta f_d \approx -\frac{2}{0.05547}\times 10 \;\approx\; -361\ \text{Hz}.
Interpretation: relative to nearby stationary sea clutter, the ship’s Doppler centroid is ~–360 Hz (sign flips with look direction). Plugging that back:
vaz≈−0.055472×(−360) ≈ 10.0 m/s.v_{az}\approx -\frac{0.05547}{2}\times(-360)\ \approx\ 10.0\ \text{m/s}.
# Example 2 — quick look-up values
- vaz=5 m/s⇒Δfd≈−180 Hzv_{az}=5\,\text{m/s}\Rightarrow \Delta f_d\approx -180\,\text{Hz}
- vaz=10 m/s⇒Δfd≈−361 Hzv_{az}=10\,\text{m/s}\Rightarrow \Delta f_d\approx -361\,\text{Hz}
- vaz=15 m/s⇒Δfd≈−541 Hzv_{az}=15\,\text{m/s}\Rightarrow \Delta f_d\approx -541\,\text{Hz}
# Estimation precision (rule of thumb)
Velocity error scales with Doppler-centroid error:
δvaz=λ2 δfd≈0.0277 m/s per Hz.\delta v_{az}=\frac{\lambda}{2}\,\delta f_d \approx 0.0277\ \text{m/s per Hz}.
So if you can estimate the centroid to ±10 Hz, that’s about ±0.28 m/s in along-track speed. Achievable δfd\delta f_d depends on SNR and the effective aperture time over which you compute the centroid (longer is better, but limited by TOPS burst geometry and ship maneuvering).
# What this gives you (and what it doesn’t)
- From a single Sentinel-1 image, you reliably get the along-track component vazv_{az} from Δfd\Delta f_d.
- The radial (range) component generally isn’t directly available from one pass without specialized processing/assumptions (e.g., model-based refocusing, external AIS, or multi-pass/ATI setups).
- Combine the along-track estimate with AIS heading/speed (when available) to recover the full 2D velocity vector and validate detections.
If you share a sample scene (burst, mode, incidence/look side) or a measured Δfd\Delta f_d from your processor, I can compute the velocity on the spot and sanity-check expected uncertainty.